## Slide 1
Appendix
Fundamentals, safe state, fits, schematics

## Slide 2
Safe state and failure modes
Jasper Buntinx | RoomCleaner | Appendix
Event | What happens | Mitigation
PAUSE, or a fault the software detects | Every station holds position with torque on | Nothing moves again without approval
Wi-Fi link lost | Stations stop and hold on their own clocks | Resume needs approval
Power loss or emergency stop | Torque is lost and the claw can fall (1.5 kg from about 2 m) | Nobody underneath; claw parked low when idle; brake planned
Controller reset or brown-out | Driver disabled at boot, so torque is lost | Same as power loss
Driver over-temperature | The A4988 shuts its outputs off | Hold test watches the driver; fallback 1.35 A
Three-station run: any station fault | Every cable is needed; the claw falls | Floor clear and padded; movement and calibration only
Notes: The safe state is PAUSE: torque on, holding. Anything that removes power drops the claw, which is why nobody stands under it and why a brake or a non-backdrivable stage is on the next-steps list.

## Slide 3
Heat fin length
CALCULATED
Jasper Buntinx | RoomCleaner | Appendix
Calculated (calc sheet: Heat fin)
0.019 in prototype reaches 95 % of its capacity by 136 mm
1/8 in design keeps gaining to 349 mm
Built at 200 mm, limited by ceiling clearance
Fin length and efficiency
m = √(2h / (k t)), L95 = 1.83 / m
η = tanh(mL) / (mL) = 0.74 (1/8 in)
Notes: L95 is where a fin carries 95 % of the heat an infinitely long one would. h = 7 W/m²·K still air, k = 160 W/m·K aluminum. Source: Incropera, ch. 3.

## Slide 4
Fin sizing for 4 W
CALCULATED
Jasper Buntinx | RoomCleaner | Appendix
Painted 6061, 44 mm wide | Mass | Shortest for ≤ 60 °C
0.019 in (prototype) | 14 g | None (2.0 W max)
1/16 in | 47 g | None (3.6 W max)
0.090 in | 68 g | 210 mm or none
1/8 in (design) | 94 g | 145–185 mm
3/16 in | 141 g | 125–140 mm
1/4 in | 189 g | 115–125 mm
All 4.05 W through the fin, 23 °C room, paste contact. Calculated.
If the fin alone had to carry all 4.05 W
0.019 in sheet: not possible at any length
1/8 in plate: 145–185 mm
Notes: The prototype works today only because the motor also sheds heat into the vented shell. Thickness beats length.

## Slide 5
Floor board accuracy
SIMULATED
Jasper Buntinx | RoomCleaner | Appendix
Calculated (calc sheet: Floor board)
Camera pose error per frame, best case: 6.6 mm with one tag, 0.7 mm with four
This is the camera's view, not the cable length
After the fit, cable lengths are known to about 12–16 mm (simulated)
Notes: Noise model: 0.3 px corner noise and a 520 px focal length (camera not yet calibrated). The four-tag figure is the best placement; realistic placements are a few times worse.

## Slide 6
Operating sequence
SIMULATED
Jasper Buntinx | RoomCleaner | Appendix
Phone app in simulation: home, claw camera and chat
Start up: self-check, take up slack, calibrate
Find: scan from above, detect garments, choose the nearest
Pick: hover until still, grip, deliver; the camera confirms each step
Every move waits for approval on the phone; PAUSE holds position
Notes: PAUSE or a detected fault stops every station on the same point of the path, still holding; nothing restarts by itself. The emergency stop is the switched power strip, and it drops the claw. Known obstacles are keep-out shapes checked against every cable before a move. Simulated end to end.

## Slide 7
Control logic: Generation 1 vs. final
Jasper Buntinx | RoomCleaner | Appendix
 | Generation 1 | Final
Where is the claw? | Assumed from the commanded cable lengths | Measured by the claw camera; refit at every startup
Room geometry | Anchors from a tape measure | Anchors and cable lengths fitted, with error bars
Motor control | One central board | A controller per station, coordinated by the laptop
Finding laundry | Ceiling camera | Claw camera
Did the grab work? | Assumed | Camera checks pickup and delivery
Faults | Emergency stop only | PAUSE keeps torque; the emergency stop cuts power and drops the claw
Notes: Generation 1 trusted its model; the final logic measures before it trusts and checks after it acts.

## Slide 8
Manufacturing: fits and datums
Jasper Buntinx | RoomCleaner | Appendix
Gear: Ø14.000 entry lip, 8 T-slots
Cut open: 687 bearing on the printed pin
Slide-in rib in the wall-mount dovetail
End-stop switch pressed into the slide-in
v3 spool: D-bore and set-screw hole
Fin: holes drilled from the first hole
My SolidWorks parts; blue and tan are cut faces, dark grey the bought bearing
Feature | As drawn | Fit
Gear bearings (687) | Ø14.075 pocket behind a Ø14.000 lip, 1.95 long, 8 T-slots | Snaps past the lip, +0.075 behind it
Gear pins | Printed Ø7.000 pin into a Ø7.05 socket | Line-to-line in the bearing; +0.05
Slide-in mount | 0.175 per side; 30° dovetail flanks | Slip fit, 0.14–0.21 on the flanks
Spool on Ø5 D-shaft | Ø5.30 bore (10/21), Ø5.45 in v3; 0.5 mm flat | +0.30 to +0.45: Ø5.2 printed too tight
End-stop switch | Pocket 6.65 × 20.3 × 9 on a 1 mm ledge, lever window below | Press fit, no screws
Heat-set inserts | M3: Ø4.0 × 5 gear housing; M2.5: Ø3.45 × 4 encoder | Melt-in; hole deeper than the insert
Screw clearance | M3 Ø3.5 printed, Ø3.4 drilled; wall Ø3.97 (5/32 in) | +0.5 printed, +0.4 drilled
Motor pilot, Ø22 boss | Ø22.4 printed tab, Ø22.5 drilled fin | +0.4 / +0.5
Fin hole zero | Edges locate the bottom-left hole; drilled, it is the zero for the other 4 | Pattern ±0.1, free of the ±0.5 sheared edges
Printed holes come out small, so every printed fit carries an allowance; the drilled fin needs none
PETG on a Creality K1, 0.4 mm nozzle, 0.2 mm layers; loads along the layers, mating faces off supports
Notes: The gear pockets: the bearing presses past a lip, the T-slots let the lip ends flex, and it then sits free in a pocket 0.075 mm larger. The slide-in runs on 0.175 mm a side. The fin's sheared edges are only good to half a millimetre, so they locate only the first hole; the rest are drilled from it. [[confirm which spool bore is printed, which holes get heat-set inserts, and the insert part number]]

## Slide 9
Station electronics, Rev D
Jasper Buntinx | RoomCleaner | Appendix
Station Rev D schematic
One board per station: a Wi-Fi microcontroller, the A4988 driver, a 12 V to 5 V buck, the homing switch and the spool encoder
Pull-up on ENABLE keeps the driver off at boot; pull-downs on STEP and DIR; a 100 µF reservoir at the driver supply
Fuses at the source end of each 12 V branch; the buck is rated to 20 V in, so the supply stays at 12 V
Notes: The external 10k pull-up on ENABLE is the reason a reset cannot move a motor; it is also why disabling removes torque, so the pull-up cannot hold a suspended load. The bench script on the Act 5 slide checks each part of this board in turn.

## Slide 10
Station breadboard layout
Jasper Buntinx | RoomCleaner | Appendix
Station Rev D breadboard layout, drawn and net-checked
The bench build of Rev D on a mini breadboard: the layout was net-checked against the schematic (PASS) before power
Each motor coil carries about 1 A through breadboard contacts: short leads, fully seated
The soldered perfboard and the rail board follow the same net list
Notes: The second bench board (the larger dev module) uses the same layout with the module off the board and nine jumpers into the holes of the small board.

## Slide 11
Claw electrical, Rev B
Jasper Buntinx | RoomCleaner | Appendix
Claw Rev B schematic
Two-cell lithium-ion pack, 7.4 V; 5 A fuse for shorts
6 V servo rail and a separate 5 V logic rail; 200k/100k divider for battery sense
Peak draw 2.8–3.1 A, at the pack's 3 A rating
Notes: Rules check 0 errors; 9 nets match the specification. Charger: 8.4 V constant current, constant voltage; charged attended, at 1 A or less. The peak sits at the pack rating, so a stall longer than a moment is the thing to watch. On the bench (10/26): live view, 7.2 V battery read, servo moves once it had its own timer.

## Slide 12
Acronyms
Jasper Buntinx | RoomCleaner | Appendix
Term | Meaning
CAD | Computer-aided design
PETG | Polyethylene terephthalate glycol (the printed plastic)
TPU | Thermoplastic polyurethane (flexible printed plastic)
NEMA 17 | National Electrical Manufacturers Association motor frame, 1.7 in square
CNC | Computer numerical control
ESP32 | A Wi-Fi microcontroller family (Espressif)
A4988 | Stepper-motor driver chip (Allegro)
YOLO | “You Only Look Once”: an object-detection model family
SF | Safety factor: allowable stress divided by actual stress

## Slide 13
Calculations and sources
Jasper Buntinx | RoomCleaner | Appendix
Calculated (calc sheet: Cable tension)
All charts come from my engineering calculation sheet
Incropera et al., Fundamentals of Heat and Mass Transfer, ch. 3
Allegro MicroSystems, A4988 datasheet