## Slide 1
Appendix

## Slide 2
Safe State and Failure Modes
Jasper Buntinx | RoomCleaner | Appendix
Event | What happens | Mitigation
PAUSE, or a fault the software detects | Every station holds position with torque on | Nothing moves again without approval
Wi-Fi link lost | Stations stop and hold on their own clocks | Resume needs approval
Power loss or emergency stop | Torque is lost and the claw can fall (1.5 kg from about 2 m) | Nobody underneath; claw parked low when idle; brake planned
Controller reset or brown-out | Driver disabled at boot, so torque is lost | Same as power loss
Driver over-temperature | The A4988 shuts its outputs off | Hold test watches the driver; fallback 1.35 A
Notes: The safe state is PAUSE: torque on, holding. Anything that removes power drops the claw, which is why nobody stands under it and why a brake or a non-backdrivable stage is on the next-steps list.

## Slide 3
Heat Fin Length
Jasper Buntinx | RoomCleaner | Appendix
Calculated (calc sheet: Heat fin)
0.019 in prototype reaches 95 % of its capacity by 136 mm
1/8 in design keeps gaining to 349 mm
Built at 200 mm, limited by ceiling clearance
Fin length and efficiency
m = √(2h / (k t)), L95 = 1.83 / m
η = tanh(mL) / (mL) = 0.74 (1/8 in)
Notes: L95 is where a fin carries 95 % of the heat an infinitely long one would. h = 7 W/m²·K still air, k = 160 W/m·K aluminum. Source: Incropera, ch. 3.

## Slide 4
Fin Sizing for 4 W
Jasper Buntinx | RoomCleaner | Appendix
Painted 6061, 44 mm wide | Mass | Shortest for ≤ 60 °C
0.019 in (prototype) | 14 g | None (2.0 W max)
1/16 in | 47 g | None (3.6 W max)
0.090 in | 68 g | 210 mm or none
1/8 in (design) | 94 g | 145–185 mm
3/16 in | 141 g | 125–140 mm
1/4 in | 189 g | 115–125 mm
All 4.05 W through the fin, 23 °C room, paste contact. Calculated.
If the fin alone had to carry all 4.05 W
0.019 in sheet: not possible at any length
1/8 in plate: 145–185 mm
Notes: The prototype works today only because the motor also sheds heat into the vented shell. Thickness beats length.

## Slide 5
Floor Board Accuracy
Jasper Buntinx | RoomCleaner | Appendix
Calculated (calc sheet: Floor board)
Camera pose error per frame, best case: 6.6 mm with one tag, 0.7 mm with four
This is the camera's view, not the cable length
After the fit, cable lengths are known to about 12–16 mm (simulated)
Notes: Noise model: 0.3 px corner noise and a 520 px focal length (camera not yet calibrated). The four-tag figure is the best placement; realistic placements are a few times worse.

## Slide 6
Operating Sequence
Jasper Buntinx | RoomCleaner | Appendix
Phone app: home, live claw camera and chat
Start up: self-check, take up slack, calibrate
Find: scan from above, detect garments, choose the nearest
Pick: hover until still, grip, deliver; the camera confirms each step
Every move waits for approval on the phone; PAUSE holds position
Notes: PAUSE or a detected fault stops every station on the same point of the path, still holding; nothing restarts by itself. The emergency stop is the switched power strip, and it drops the claw. Known obstacles are keep-out cylinders checked against every cable before a move. Simulated end to end.

## Slide 7
Control Logic: Generation 1 vs. Final
Jasper Buntinx | RoomCleaner | Appendix
 | Generation 1 | Final
Where is the claw? | Assumed from the commanded cable lengths | Measured by the claw camera; refit at every startup
Room geometry | Anchors from a tape measure | Anchors and cable lengths fitted, with error bars
Motor control | One central board | A controller per station, coordinated by the laptop
Finding laundry | Ceiling camera | Claw camera
Did the grab work? | Assumed | Camera checks pickup and delivery
Faults | Emergency stop only | PAUSE keeps torque; the emergency stop cuts power and drops the claw
Notes: Generation 1 trusted its model; the final logic measures before it trusts and checks after it acts.

## Slide 8
Claw Electrical
Jasper Buntinx | RoomCleaner | Appendix
Claw schematic
Two-cell lithium-ion pack, 7.4 V; 5 A fuse for shorts
6 V servo rail and a separate 5 V logic rail
Peak draw 2.8–3.1 A, at the pack's 3 A rating
Notes: Rules check 0 errors; 9 nets match the specification. Charger: 8.4 V constant current, constant voltage; charged attended, at 1 A or less. The peak sits at the pack rating, so a stall longer than a moment is the thing to watch.

## Slide 9
Acronyms
Jasper Buntinx | RoomCleaner | Appendix
Term | Meaning
CAD | Computer-aided design
PETG | Polyethylene terephthalate glycol (the printed plastic)
TPU | Thermoplastic polyurethane (flexible printed plastic)
NEMA 17 | National Electrical Manufacturers Association motor frame, 1.7 in square
CNC | Computer numerical control
ESP32 | A Wi-Fi microcontroller family (Espressif)
A4988 | Stepper-motor driver chip (Allegro)
YOLO | “You Only Look Once”: an object-detection model family
SF | Safety factor: allowable stress divided by actual stress

## Slide 10
Calculations and Sources
Jasper Buntinx | RoomCleaner | Appendix
Calculated (calc sheet: Cable tension)
All charts come from my engineering calculation sheet
Incropera et al., Fundamentals of Heat and Mass Transfer, ch. 3
Allegro MicroSystems, A4988 datasheet